Counter synchronised by GPS

KAKL

There is a counter for measuring frequency up to 600 MHz with absolute precision ±15 Hz at maximum frequency (±25 ns / 1 s).

# Technical parameters

| Parameter | Value | Note |
| --- | --- | --- |
| Minimal frequency | 4 Hz | There is a systematical error -3 Hz |
| Maximal Frequency | 640 Hz | Computer room |
| Time accuracy | ±25 ns / 1 s | By given GPS |

# Construction

## Connection

## Used modules

- S3AN01B

- GPS01A

- TTLPECL01A

## Hack

Two 50 Ω resistors from SATA connector to +1.2 V has to be added.

# Text boxes

JTAG

LVPECL / TTL

Converter

GPS

Measured Crystal 50 MHz

Half/Full frequency Switch

1PPS signal

100 of MHz

GPS antenna

1 of Hz